## Slide 1
Use of millimeter and optical wavelengths for next generation aerospace communication systems
Carlo Capsoni
Dipartimento Elettronica, Informazione e Bioingegneria, Politecnico di Milano
IN Florence- Italy
22-June-2016

## Slide 2: Outline
Introduction
Satellite TLC systems
present (MW)
future (MW)
future (optical)
Aeronautical TLC systems
present (MW)
future (optical)
Conclusions
<number>
Notes: <number>

## Slide 3: Introduction
Anytime, anywhere access to multimedia systems requires higher datarate to distribute high speed Internet access, video streaming, file transfer, multimedia applications…….
SATCOM systems are appealing because because of the global coverage in the service area, provided that the cost/bit is competitive with respect to other services
Higher datarates requires more bandwidth and therefore higher carrier frequencies (and obviously very efficient modulations/coding)
Higher frequencies means more troubles to face because of the increasing propagation impairments due to the troposphere
<number>
Proper design of next SATCOM systems based on advanced FMTs

## Slide 4
SATELLITE TLC SYSTEMS
MICROWAVE CARRIER FREQUENCIES
<number>

## Slide 5: Spectrum considerations
<number>
Band |  | ranges (GHz) | notes
Ka | up link | 29.5-30 (excl.) 27.5-29.5 (shared) 24.75-25.25 (shared) | 3 GHz with restrictions
Ka | down link | 19.7-20.2 (exc.) 17.3-19.7 (shared) 21.4-22 (shared) | 3 GHz with restrictions
Q/V | up link | 42.5-43.5 (shared) 47.2-50.2(shared) 50.4-51.4 (shared) | 5 GHz with restrictions
Q/V | down link | 37.5-39.5(shared) 40.5-42.5 (shared) | 4 GHz with restrictions
W | up link | 81-86 (excl.) | 5 GHz with no restrictions
W | down link | 71-76 (excl.) | 5GHz with no restrictions

## Slide 6: Present configuration
One satellite per service area
Some few GWs (10/12) spread over the service area and connected to the Internet backbone (fibre optic)
End users directly connected to the satellite through a multibeam antenna ( more than 70 beams per reflector) for frequency reuse purposes.
Kasat
82 spotbeam towards the end users
10 GWs
> 90GBps
22/6 MBps upload/download
for the end user
50/10 MBps upload/download
for professional
<number>

## Slide 7: Future configuration: system design
LINK BUDGET
In addition to deterministic losses (FSL, WG , mispointing,….)
There are statistical contributions due to atmospheric impairments:
Gases attenuation (absorption due to molecular resonance of Oxygen and Water Vapour)
Clouds attenuation (absorption due to water particles much smaller than )
Rain attenuation (absorption and scattering due to hydrometeors which size is of the same order of magnitude of )
Clear air effects (scintillation) have relatively marginal impact
<number>
The standard approach to oversize the system (TX powers, antennas size) is almost impossible to apply and in any case inefficient
Smart techniques (FMT) should be used to counteract system degradation

## Slide 8: Future configuration: system design
<number>
Attenuation CCDF: Clouds (left) and of rain (right). 30 deg slant path. Site: Milan

## Slide 9: Fade Mitigation Techniques: GW side
In addition to the standard satellite FMTs (ULPC..), site diversity configuration is a very promising technique:
small scale ( GWs distance in the order of 50 to max 100km) not convenient; backup is on a one-to-one basis
<number>
large scale diversity convenient although complex to handle
Solution N+P: some extra GWs are added and become active only when any one of the network GWs is out of service
Solution N+0: the traffic of the impaired GW is redirected to other GW(s) of the network

## Slide 10: Fade Mitigation Techniques: large scale diversity
<number>
GW4 Outage
GW7 Outage
GW4 Outage

## Slide 11: Fade Mitigation Techniques: user side
Use of multibeam antenna to cover the service area
  Frequency and/or polarization reuse to reduce interbeam interference
ACM
On-board reconfigurable antenna
Key parameter: SNIR
<number>

## Slide 12: Fade Mitigation Techniques: user side
Use of multibeam antenna to cover the service area
  Frequency and/or polarization reuse to reduce interbeam interference
ACM
On-board reconfigurable antenna
Key parameter: SNIR
<number>

## Slide 13: Fade Mitigation Techniques: user side
On-board reconfigurable antenna
<number>
Actual Attenuation Map (Spatial Prob. A >2 dB)
Power Margin @ Ground
(Reconfigurable)
Power Margin @ Ground
(Fixed Front-end)
Widespread rain
Convective cells

## Slide 14: Future configuration (example)
Coverage: EU27
Up link in Q/V band (4 GHz in each polarization)
Each GW covers several EU beams
GW availability: 99.9%, DVB-S2 with 32 APSK 5/6 with a spectral efficiency of 3.43b/s-Hz
19 GWs minimum + diversity GWs for counteract atmospheric impairments (N+P)
Down link in Ka band (2.5GHz)
User link availability: 99.7% DVB-S2/RCS2 APSK 5/6 with a spectral efficiency of 3.43b/s-Hz
88 beams in dual polarization or 116 in single polarization, minimum
Key element: antenna design
<number>

## Slide 15
SATELLITE TLC SYSTEMS
OPTICAL CARRIER
<number>

## Slide 16: System design
LINK BUDGET
Use of optical carriers require a completely different approach to the design of Satellite TLC systems
Rain (3-7% yearly probability) is no more the most impairing phenomenon
Clouds (30-70% yearly probability) and fog (very variable site dependent occurrence) are the very limiting factors
Clear air turbulence is important and has to be taken in due account
Gases attenuation (mainly water vapor and carbon dioxide) identifies specific usable windows
<number>
0.850 m, 1.064 m, 1.550 m wavelengths in use today
10.6 m future use (?)

## Slide 17: System design
<number>
Water cloud attenuation (scattering due to droplets which size is larger than )
Ice cloud attenuation is limited
100 dB cloud attenuation exceeded for 10% of yearly time
50 dB cloud attenuation exceeded for 15% of yearly time
Low contribution of ice to total attenuation (e.g. Aice / Aliq ≈ 16 for P = 10%)
Cloud attenuation at 10.6 m is definitely smaller than at 1.55 m (effect is mostly
noticeable at higher probabilities)

## Slide 18: System design
Rain attenuation (scattering due to droplets which size is much larger than ) is of the same order of magnitude as at MW (Q/V) low occurrence probability
Atmospheric turbulence produces intensity (and phase) fluctuations as well as beam wander responsible of strong fading
<number>

## Slide 19: Fade Mitigation Techniques
Differently from the MW solution where most GWs are operative and few are eventually out of work, in the OPTICAL solution few GWs (1,2) are operative and the others are out of work.
Large scale site diversity is the only approach to use
Example
<number>

## Slide 20: Future configuration
<number>
cloud
Optical stations
User terminals
RF link

## Slide 21: Future configuration (example)
Coverage EU27 and Turkey with two geostationary satellites colocated
Each GW covers several EU beams
Gw availability: 99.9% DVB-S2 using Dense Wavelength division Multiplexing (DWDM)
17/18 dB margin wrt clear sky conditions ((to counteract, scintillation and ice cloud attenuation)
2 OGS using 90 nm total BW (forward + return)
800 Gbps in the forward link and 249 Gbps in the return link
12 GWs in site diversity configuration
Down link in Ka band (1.45 GHz)
User link availability: 99.7% DVB-S2/RCS2
151 beams per satellite of 0.21deg beamwidth
4 colors frequency reuse scheme
MFPB configuration with 5 m class antenna (different antennas for transmit and receive links)
<number>

## Slide 22: Future configuration (example)
GWs position identification
German network based on 22 selected sites with average station availability of 30%
12 GWs network availability: 84.7%
European network based on 26 selected sites with ½ stations with availability >50%
12 GWs network availability of 99.9%
Intercontinental network based on 16 selected sites with stations availability ranging from 50% to 80%
8 GWs network availability of 99.9%
9 GWs network availability of 100%
Analysis based on 5 years MSG cloud coverage
J.OPT. COMMUN NETW: vol.7,n.12. Dec. 2015
<number>

## Slide 23
AERONAUTICAL TELECOMMUNICATION SYSTEMS
<number>

## Slide 24: Present configuration
Air travellers are asking for global access to high speed Internet during the flight
Aeronautical telecommunication needs are increasing due to passenger request and other airline communication services (weather forecast, real time monitoring,…)
Air-to-ground connectivity is available today on flights over continents (few MHz in the 800 MHz band with future plans to have 500 MHz available in the 14-14.5 GHz range)
Alternatively, on-board Internet access is based on satellite services operating in the MW region
The bitrate capacity per aircraft is in the order of Mbit/s, with a limited possible expansion because of the non-exclusive use and finite availability of radio frequency spectrum (ca. 16 GHz in Ku- and Ka-band).
Due to the complex infrastructure, satellite service is relatively expensive.
<number>

## Slide 25: Future configuration
Present situation not satisfactory push for the identification of more complex systems
MW satellite service
  dedicated LEO HTS in Ku/Ka bands
  but SATCOM stand-alone service is expected to have capacity limitations
Broadband airborne network
  hybrid air-to-air-to-ground communication system using high performance FSO for highest capacity and robust MW communication for weather mitigation.
In-cabin use of VLC for user connectivity instead of standard WiFi
<number>

## Slide 26: Aircraft network in FSO
<number>
HAP (network sink)
Aircraft
Velocity vector
Optical link
Simulated scenario: North Atlantic corridor
Aircraft network connected to ground through HAPs (primary)+ satellite for capacity alleviation and support for link obstruction by clouds (secondary)
Ground-to-HAP links: OPTICAL +MW
Network through aircrafts: OPTICAL (Hybridization MW+OPT to be considered)

## Slide 27: Aircraft network in FSO
<number>
HAP (network sink)
Aircraft
Velocity vector
Optical link
Simulated scenario: North Atlantic corridor
Size: 5000x3000 km2
Aircraft density 3x10-5km2
Communication range of 300km average connectivity in the order of 99.8%
Shorter communication range reduced connectivity
4th IWOW 2015

## Slide 28: Conclusions
HTS systems for anytime, anywhere access to multimedia systems requires higher datarate /carrier frequencies
SATCOM appealing because of the global coverage have to move to Q/V or even W band for GWs-to-satellite connection in MW range or to OPTICAL wavelengths
Large scale site diversity configuration is mandatory for GWs; use of reconfigurable antenna under study
Aeronautical TLC needs are increasing due to passenger request (global access to high speed Internet during flight) and other airline communication services
Present situation based on direct Air-to-ground connectivity or SATCOM systems not satisfactory.
Dedicated LEO HTS in Ku/Ka bands but SATCOM stand-alone service is expected to have capacity limitations
  Broadband airborne network using high performance FSO for highest capacity and robust MW communication for weather mitigation.
  In-cabin use of VLC for user connectivity instead of standard WiFi
<number>